## Slide 1: Example : Floating Point Adder Unit

## Slide 2: Floating Point Adder Unit
This pipeline is linearly constructed with 4 functional stages.
The inputs to this pipeline are two normalized floating point numbers of the form
A = a x 2p
B = b x 2q
where a and b are two fractions and p and q are their exponents.
For simplicity, base 2 is assumed

## Slide 3: Floating Point Adder Unit
Our purpose is to compute the sum
C = A + B = c x 2r = d x 2s
where r = max(p,q) and 0.5 ≤ d < 1
For example:
A=0.9504 x 103
B=0.8200 x 102
a = 0.9504 b= 0.8200
p=3 & q =2

## Slide 4: Floating Point Adder Unit
Operations performed in the four pipeline stages are :
Compare p and q and choose the largest exponent, r = max(p,q)and compute t = |p – q|
Example:
r = max(p , q) = 3
t = |p-q| = |3-2|= 1

## Slide 5: Floating Point Adder Unit
Shift right the fraction associated with the smaller exponent by t units to equalize the two exponents before fraction addition.
Example:
Smaller exponent, b= 0.8200
Shift right b by 1 unit is 0.082

## Slide 6: Floating Point Adder Unit
Perform fixed-point addition of two fractions to produce the intermediate sum fraction c, where 0 ≤ c < 1
Example :
a = 0.9504 b= 0.082
c = a + b = 0.9504 + 0.082 = 1.0324

## Slide 7: Floating Point Adder Unit
Count the number of leading zeros (u) in fraction c and shift left c by u units to produce the normalized fraction sum d = c x 2u, with a leading bit 1. Update the large exponent s by subtracting s = r – u to produce the output exponent.
Example:
c = 1.0324 , u = -1  right shift
d = 0.10324 , s= r – u = 3-(-1) = 4
C = 0.10324 x 104

## Slide 8: Floating Point Adder Unit
The above 4 steps can all be implemented with combinational logic circuits and the 4 stages are:
Comparator / Subtractor
Shifter
Fixed Point Adder
Normalizer (leading zero counter and shifter)

## Slide 9: Example for floating-point adder
Exponents
Segment 1:
Segment 2:
Segment 3:
Segment 4:
R
R
R
R
R
R
R
R
Adjust
exponent
Normalize
result
Add
mantissas
Align mantissas
Choose exponent
Compare
exponents
by subtraction
Difference=3-2=1
Mantissas
b
a
A
B
For example:
X=0.9504*103
Y=0.8200*102
0.082
3
S=0.9504+0.082=1.0324
0.10324
4