## Slide 1: Types of Cache Misses: The Three C’s
Compulsory: On the first access to a block; the block must be brought into the cache; also called cold start misses, or first reference misses.
Capacity: Occur because blocks are being discarded from cache because cache cannot contain all blocks needed for program execution (program working set is much larger than cache capacity).
Conflict: In the case of set associative or direct mapped block placement strategies, conflict misses occur when several blocks are mapped to the same set or block frame; also called collision misses or interference misses.

## Slide 2: Miss Rate Reduction Techniques:
  Increased cache capacity
  Larger block size
  Higher associatively
  * Compiler optimizations

## Slide 3: Miss Rate Reduction Techniques: Reduce Misses by Larger Block Size
A larger block size improves cache performance by taking advantage of spatial locality
For a fixed cache size, larger block sizes mean fewer cache block frames
  Performance keeps improving to a limit when the fewer number of cache block frames increases conflict misses and thus overall cache miss rate

## Slide 4: 2. Reduce Misses by Increasing Cache Size
Increasing cache size reduces cache misses
  both capacity misses and conflict misses reduced

## Slide 5: Miss Rate Reduction Techniques: Higher Cache Associativity
    Reduces conflict misses
Cache Size Associativity
(KB) 1-way 2-way 4-way 8-way
1 2.33 2.15 2.07 2.01
2 1.98 1.86 1.76 1.68
4 1.72 1.67 1.61 1.53
8 1.46 1.48 1.47 1.43
16 1.29 1.32 1.32 1.32
32 1.20 1.24 1.25 1.27
64 1.14 1.20 1.21 1.23
128 1.10 1.17 1.18 1.20
(Red means A.M.A.T. not improved by more associativity)

## Slide 6: Miss Rate Reduction Techniques: Compiler Optimizations
Compiler cache optimizations improve access locality
characteristics of the generated code and include:
Merging Arrays: Improve spatial locality by single array of compound elements vs. 2 arrays.
Loop Interchange: Change nesting of loops to access data in the order stored in memory.
Loop Fusion: Combine 2 or more independent loops that have the same looping and some variables overlap.
Blocking: Improve temporal locality by accessing “blocks” of data repeatedly vs. going down whole columns or rows.

## Slide 7: Merging Arrays
/* Before: 2 sequential arrays */
int val[SIZE];
int key[SIZE];
/* After: 1 array of stuctures */
struct merge {
int val;
int key;
};
struct merge merged_array[SIZE];
combines two separate arrays (that might conflict for a single block in the cache) into a single interleaved array.
    This brings together corresponding elements in both arrays, which are likely to be referenced together.
    reduces misses by improving spatial locality.

## Slide 8: Miss Rate Reduction Techniques: Compiler-Based Cache Optimizations Loop Interchange Example
/* Before */
for (k = 0; k < 100; k = k+1)
for (j = 0; j < 100; j = j+1)
for (i = 0; i < 5000; i = i+1)
x[i][j] = 2 * x[i][j];
/* After */
for (k = 0; k < 100; k = k+1)
for (i = 0; i < 5000; i = i+1)
for (j = 0; j < 100; j = j+1)
x[i][j] = 2 * x[i][j];
Sequential accesses instead of striding through memory every 100 words in this case improves spatial locality.

## Slide 9: Miss Rate Reduction Techniques: Compiler-Based Cache Optimizations Loop Fusion Example
/* Before */
for (i = 0; i < N; i = i+1)
for (j = 0; j < N; j = j+1)
a[i][j] = 1/b[i][j] * c[i][j];
for (i = 0; i < N; i = i+1)
for (j = 0; j < N; j = j+1)
d[i][j] = a[i][j] + c[i][j];
/* After */
for (i = 0; i < N; i = i+1)
for (j = 0; j < N; j = j+1)
{ a[i][j] = 1/b[i][j] * c[i][j];
d[i][j] = a[i][j] + c[i][j];}
Many programs have separate loops that operate on the same data.
Combining these loops by grouping operations on the same (cached) data together.