## Slide 1: Ripple Carry Adder Gate Delay

## Slide 2
Delay in getting Ci+1 from time when Ci enters is 2 gate delays
Si available after 1 gate delay

## Slide 3
Cn got after 2n gate delays
Sn-1 got after 2n-1 gate delays from time when C0 enters RCA
n=8, 8 bit addition , sum available after 15 gate delays

## Slide 5: Gate Delays in Ripple Carry Adder/Subtractor
In adder/subtractor
  Sum/difference available after 2n-1 +1(for the xor gate used in add/sub control= 2n gate delays
  and Cn after 2n +1 gate delays
  Plus another xor gate checks for overflow
  So Cn available after 2n+2 gate delays
    For 8 bit adding C8 available after 18 gate delays!!